## Slide 1: P- 705A/B Root Cause of Failure analysis

## Slide 2: Outline
Pump Overview
Objective
Process flow diagram (PFD)
Root cause analysis
Suggestion
Action Taken
Observations after implementation

## Slide 3: Problem
Frequent mechanical seal failure of P-705 A/B (Loop reactor circulation pump)

## Slide 4: Pump overview
Location: Ground floor loop reactor
Purpose of pump: To circulate material across loop reactor and steam generator
Pump Specifications
Tag. No | P-705 B | P-705 A
Make | KSB | RHUR PUMPEN GMBH
Model | RPH-01-250-501 | SV N8-8 X 22
Sr.No | 5111026205/100/02 | 
Flow | 400 | 400
Pressure |  | In =23.12, out=26.04
Head | 36 | 35
Power | 44.4 | 44.4
Speed | 987 | 990
Motor KW | 55 | 55

## Slide 5: PFD
Loop Reactor
Steam generator
P-705 A
LCV-302
XV-311
From
P-705 B

## Slide 6: Root Cause analysis
Sr. No. | Seal Drawing No | Seal Type | Average Seal life | Problem Reported | Observation | Suspected Root Cause | Action Taken
1 | Burgmann MFC/85N | Multi-Spring type | 1 month | IB and OB seal leakage | O-Ring Extrusion and IB Seal Hang up. | IB Seal Hang up due to In-effective flow and nickel catalyst causing O-Ring Extrusion | Approached Eagle Poonawala for the problem, recommended EPIL Y9 D56/D64
2 | Y9 D56/D64-B01917 AA | Bellow Type | 4-5 months | Seal leakage from shaft and sleeve | Sleeve design not proper | Sleeve dimensions not proper | Changed sleeve Dimensions
3 | Y9 D56/D64-B01917 AA | Bellow type | 4-5 months | Frequent seal leak | IB and OB seal Leakage | IB Seal Hang up. Material Clogging Near IB seal. | Approached Jhon Crane for the same, recommended their 48 VRS/ 48 VRS dual seal on trial basis with plan 54.
4 | GA-169435 | Multi-Spring type | 1 month | Seal Leakage | IB Seal Leakage. | Ineffective flusing in IB area. | Installed EBIL seal Y9 D56/ D64
5 | GA-169435 | Multi-Spring type | 1 and half month | Seal Leakage | Seal Leakage |  | Seal Installed after reconditioning from Jhon Crane. Seal leaked after around 1 and half months. EBIL Seal Y9 D56/D64 installed back on pump.
P-705A

## Slide 7
Sr. No. | Seal Drawing No | Seal Type | Average seal life | Problem Reported | Observation | Suspected Root Cause | Action Taken
1 | 09-H75VKP-D1/95 | Multi Spring Type | 2-3 months | IB Seal Leakage | IB Seal Ring Cutting | In- effective Circulation | 1. Steam jacketing Provided to Barrier Fluid Inlet and outlet Piping
 |  |  |  |  |  |  | 2. Barrier fluid Changed from pure glycerin to 80% Glycerin + 20% water
 |  |  |  |  |  |  | 3. SOP for API plan 53 B Altered
2 | 09-H75VKP-D1/95 | Multi Spring Type | 2-3 months | IB Seal Leakage | IB seal hang up | IB DA type MR squareness | MR changed to CS type
3 | 09-H75VKP-D1/95 | Multi Spring Type | 2-3 months | IB Seal Leakage | OB viton O-rings getting square in shape | OB o-ring MOC | OB o-ring MOC changed from Viton to FFKM kalrez (200&260)
4 | 09-H75VKP-D1/95 | Multi Spring Type | 1-2 months | IB Seal Leakage | IB seal ring face catalyst or metal deposition | IB face MOC | IB face changed from Carbon to SiC.
5 | 09-H75VKP-D1/95 | Multi Spring Type | 1-2 months | IB Seal Leakage | IB O ring Extrusion | In Effective flow | Flow distributor provided inside seal housing and pumping ring type changed from pedal type to screw type. Drawing revised from H75 VKP to H75 VKF
P-705B

## Slide 8: Suggestion
As provision to gradually start pump which can lead to seal failure, Soft-starter should be installed
As observes from past observation data and present observation, chances of human error during batch transfer can lead sudden decrease in pump suction pressure so Operators should be instructed to take extra precaution before initiating batch transfer process (i.e. Operator should stop pump without fail before opening transferring valves)
mechanical seal of the both pumps should be checked by mechanical department

## Slide 9: Action Taken
Mechanical seal design of both pumps ( P-705A & P-705B) is changed in July – 2016 .
Observation After Implementation
MTBF (mean time between failure) of both pumps initially 1.5 months is changed to 8 months (from July2016 to March 2016 ) still working without any failure

## Slide 10: Thank You !!!