## Slide 1: VVF INDIA LTD
HYDROGEN PEROXIDE (H2O2) PRE-FEASIBILITY REPORT

## Slide 2: Why H2O2
Chart: VVF NG CONSUMPTION REPORT
| GAIL NG contractual supply qty.scm/day | VVF NG consumption Max qty. scm/day | Min Spare NG scm/day
VVF NG CONSUMPTION REPORT | 100000 | 90000 | 10000

## Slide 3: H2O2 Key Transformation process

## Slide 4: Indian Market Demand-supply scenario
Chart: H2O2 Report
| Total plant capacity MT/A | Total supply MT/A -2014-15 | Total Demand MT/A 2014-15 | Gap MT/A
FY 14-15 MT/A | 111225 | 96172 | 119800 | 23628
Current GACL ongoing Expansion of H2O2 14400MTA
Still gap found 9228MTA

## Slide 5: H2O2 Need for Indian Market
Chart: Installed Capacity Vs Production of existing players
| NPL | GACL | APL | HOCL
Installed capacity FY14-15 MT/A | 48000 | 40000 | 18000 | 5225
Production in FY14-15 MT/A | 44111 | 38201 | 9035 | 4825

There are only four manufacturers in India .
1.Gujrat Alkalies and Chemicals Ltd.
2.National Peroxide Ltd
3.Asian Peroxide Ltd
4.Hindustan Organic Chemicals Ltd.

## Slide 6: Global Market Trend

## Slide 7: Forecast for the H2O2
Chart: Global demand (Million metric tons)
| 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2022
Global demand (Million metric tons) | 1.8 | 2.1 | 2.4 | 2.8 | 3.2 | 3.8 | 4.2 | 5.3 | 5.7

## Slide 8: H2o2 Regional Consumption Report
Main end Market
1 Paper & Pulp industry - 55%
2 Chemical & laundry industry -33
Regional market Share
China - 40%
Europe – 19%
North America – 12%
Other Asia – 11%
Cen//S America - 4%
Japan – 4%
Rep of Korea – 3%
India – 3%
Middle east/Africa – 2%
CIS – 1%
Taiwan – 1%

## Slide 9: Competitive landscape
Total Companies Profiled 47 | 
Region/ Country | Players
The United States | 9
Japan | 6
Europe | 9
Asia-Pacific (Excl. Japan) | 21
Latin America | 1
Middle East | 1

## Slide 10: H2O2 Introduction
Hydrogen peroxide, a weakly acidic colorless liquid, was discovered by Thenard in 1818 and has been uses industrially since the mid-19th century. Its scale of manufacture and use have increased markedly since about 1925 when electrolytic processes were introduced to the United States and industrial bleach applications were developed. Now prepared primarily by anthraquinone autoxidation (where a molecule is oxidized by oxygen), hydrogen peroxide is used widely to prepare other peroxygen compounds and as a nonpolluting oxidizing agent.

## Slide 11: Physical properties of H2O2
Property Value
melting point / degC -0.41
boiling point / degC 150.2
density at 25oC / g mL-1 1.4425
viscosity at 20oC / MPas 1.245
surface tension at 20oC / mNm-1 80.4
specific conductance at 25oC / Ω.cm 4 x 10-7
enthalpy of fusion / J g-1 367.52
specific heat at 25oC / J g-1 2.628
heat of vaporization at 25oC / J g-1 1517
pKa at 20degC 11.75
heat of dissociation / kJ mol-1 34.3

## Slide 12: Raw material consumption/MT of H2O2
Sr.No. | Raw Material | Proposed Qty./MT of H2O2
1 | Hydrogen gas | 710-730 Nm3
2 | Ethy Anthra Quinone | 0.8-1 Kg
3 | Shellsol | 0.83-5 Kg
4 | Tetra Butyl Urea | 0.5-0.8 Kg
5 | Tetra octyl phosphate | 0.16 Kg
6 | Palladium catalyst | 0.02-0.04 Kg
7 | stabillizer | 0.4-0.8 Kg
8 | Nitric acid | 0.83 Kg
9 | Phospheric acid | 0.8-1 Kg
10 | Treated alumina | 9.5-12 Kg

## Slide 13: Utility Consumption
Sr. No. | Entity | Qty./MT Of H2O2
1 | Raw Water | 0.5m3
2 | Steam | 1.7T@22 kg/cm2
3 | Compressed Air | 3394Nm3@ 3Kg/cm2
4 | Electricity | 0.7mwh

## Slide 14: H2O2 process

## Slide 15: H2O2 Process Reaction
NG Reforming- H2 ,CO2 & CO forming from NG
CH4+H2O= CO+3H2 CO+H2O=CO2+H2
Hydrogen Purification-H2 of 98.5 Purity obtain by PSA technology
CO2 & CO got removed
Hydrogenation-Enthraquinone solution is used under existence of Pd catalyst to produce hydrogenated enthraquinone.
H2+EAQ = EAQinol
Oxidation – Hydrogenated enthraquinone reacted with oxygen EAQinol + O2= H2O2 + EAQ
H2O2 Extraction - The deionized water extracts the H2O2 from oxidized solution

## Slide 16: Profit Scenario
H2O2 Production Capacity – 10KTA
Saleable H2O2 Capacity(50% Concentration )– 20KTA
H2O2 sell Price -Rs30/Kg
Total Sale - 60 crores /Annum
Profit Booked @ 10% - 6Crores/Annum

## Slide 17: 10KTA H2O2 Plant – 80 Crores
NG – 10000 scm/day
Minimum NG Availability
H2- 1000 Nm3/ hr H2- 22800Nm3/Day
H2 production per Hour and Day
730Nm3 H2 required to produce per MT of H2O2
H2O2 Production – 31.23T/Day or 11KTA cap (100% basis) plant to be built
Saleable Qty. 50% grade = 22KTA

## Slide 18
Item | Cost (Rs in Crore)
1 Technology Licensing & FEED for H2O2 | 10
2 Engineering and Construction | 10
3 Resource and Infrastructure cost | 50
4 Contingency & Escalation | 5
5 Capitalized Interest | 5
Total cost | 80
Cost Break-Up

## Slide 19: Conclusion
The current demand Gap 9 KTA Vs our proposed plant 10 KTA capacity matched which also meet our excess NG utilization of 10000 SCM/ Day
THANK YOU