## Slide 1: SUMMARY OF HAZOP STUDY – HYDROGENATION PLANT
VVF Limited
baddi industrial area, himachal pradesh

## Slide 2: NODE 1 – Fatty Acid Storage Tank
HAZARDS IDENTIFIED
Major leakage of storage tank from valves/connected pipelines/nozzles or from the road tanker fittings.
Leakage of fatty acid in the work area. It is a mild irritant to skin and eyes.
Molten product can cause burn injury on contact.
RECOMMENDATIONS
“Sufficient resources like spill kits, spare trolleys, drums etc. should be provided to contain and accumulate the leakages in the storage tank area.
Preventive maintenance such as thickness testing and visual inspections should be carried out for the storage tanks.”

## Slide 3: NODE 1 – Fatty Acid Storage Tank
HAZARDS IDENTIFIED
Operator checks the temperature of the tank by touching the tank with bare hands and adjusts the steam supply valve accordingly.
Malfunction of the PRV station - The temperature may rise to the high pressure steam temperature. Design data of the low pressure steam pipelines and the storage tank should be maintained.
RECOMMENDATIONS
“Steam pressure reducing station should be calibrated periodically.
Pressure relief valve should be provided on the downstream side of the pressure reducing station.
Temperature gauge should be provided to monitor the storage tank temperature.”

## Slide 4: NODE 1 – Fatty Acid Storage Tank
HAZARDS IDENTIFIED
Product other than required fatty acid in the storage tank due to communication error between the tank farm manager and the tank farm operator.
RECOMMENDATIONS
“Verbal communication for transfer of products from tank to the plant.
No return procedure for return of wrong product from the plant back to the storage tank.”

## Slide 5: NODE 2 – Fatty Acid Transfer Pump
HAZARDS IDENTIFIED
Many valves are to be operated at different stages. Pump suction valve, discharge valve or drain valve kept open/close against the process requirement. This will lead to dry running of the pump or churning of material inside the pump leading to seal failures and leakages.
Preventive maintenance schedule not available for pumps and motors of hydrogenation plant.
RECOMMENDATIONS
“Critical valve operation sequence should be incorporated in the hydrogenation batch sheet.
Post maintenance start-up checklist should be prepared for critical equipment failures.
Important instructions should be displayed near the pumping section.”

## Slide 6: NODE 3 – Hydrogen Gas Bank
HAZARDS IDENTIFIED
Major leakages from hydrogen cylinder valve or due to rupture of the hydrogen pipeline from the gas bank will lead to presence of highly flammable gas in the atmosphere.
RECOMMENDATIONS
“Emergency action plant for hydrogen leakage from cylinder should be prepared in and personnel should be trained.
Hydrogen gas detector should be provided near the trolley. Hydrogen gas detector should be maintained operational and should be periodically tested.
Flexible SS hose used for connection between the gas bank and PCV should be hydrotested periodically.
Flameproof electrical equipment’s provided in the hydrogen shed should be inspected periodically.
Bonding and earthing provided for the pipelines in the hydrogen shed area should be periodically checked for continuity and resistance respectively.”

## Slide 7: NODE 3 – Hydrogen Gas Bank
HAZARDS IDENTIFIED
Major leakages from hydrogen PCV station due to rupture of the pipeline or from welded joints will lead to presence of highly flammable gas in the atmosphere.
RECOMMENDATIONS
“Emergency action plant for hydrogen leakage from cylinder should be prepared in and personnel should be trained.
Control valve should be provided at the PCV station inlet. Hydrogen gas detector provided near the PCV station should be interlocked to shut down this control valve.
Hydrogen gas detector should be made operational.”

## Slide 8: NODE 3 – Hydrogen Gas Bank
HAZARDS IDENTIFIED
The pipeline may become empty after the batch completion or other maintenance activities. In such case, air may ingress in the pipeline. When the hydrogen transfer is restored, this may lead to formation of flammable fuel-air mixture.
RECOMMENDATIONS
“Nitrogen flushing of the pipeline and reactor is recommended before starting the batch e.g. before starting the vacuum application to the reactor.”

## Slide 9: NODE 3 – Hydrogen Gas Bank
RECOMMENDATIONS
“S.O.P. should be prepared which contains provisions to prevent accumulation of static electricity and periodic inspection of the earthing & bonding should be carried out. Operators should be trained about the importance of flange bonding.
The PCV - pressure gauges and safety relief valves should be periodically tested and calibrated.
The PCV system should be upgraded as mentioned in the drawing no. NI/H2/1240/P20047 R0. Control valve should be provided at the PCV station inlet. Two separate vents with flame arrestor should be provided for each set of PCV to prevent back pressure in the low pressure PCV set.”

## Slide 10: NODE 4 – Hydrogenation Reactor
HAZARDS IDENTIFIED
Vacuum system failure – Initial check of leakages through reactor and pipelines will not be possible. Also, air entrapped in the reactor will not be removed. Further on hydrogen gas addition, this will lead to formation of flammable mixture in the reactor.
RECOMMENDATIONS
“Hydrogen gas leak detector should be provided near the reactor. It should be interlocked with auto shutdown of hydrogen supply.
Preventive maintenance schedule not available for pumps and motors of hydrogenation plant.
Periodic inspection of the flameproof electrical equipment’s to be done.
Standby cooling water pump should be provided for the vacuum system.
Batch sheet should be updated with critical steps e.g. operation of cooling water pump of vacuum system.
Many valves are to be operated at different stages – Critical valve operation sequence should be incorporated in the hydrogenation batch sheet.”

## Slide 11: NODE 4 – Hydrogenation Reactor
HAZARDS IDENTIFIED
Interlock between control valve and mass flow meter malfunction. This can lead to less or more quantity of fatty acid added to the reactor.
RECOMMENDATIONS
“Calibration of the interlock between control valve and mass flow meter should be carried out.”

## Slide 12: NODE 4 – Hydrogenation Reactor
HAZARDS IDENTIFIED
Vacuum system not isolated before starting hydrogen gas. Hydrogen gas will escape through the vacuum system into the atmosphere.
RECOMMENDATIONS
“Valve operation sequence should be included in the batch records and batch check sheet e.g. to ensure that vacuum system is isolated before starting the hydrogen gas supply to the reactor.
Flange bonding and earthing required on all pipelines in which there are chances of hydrogen gas ingress.”

## Slide 13: NODE 4 – Hydrogenation Reactor
HAZARDS IDENTIFIED
Failure of the cooling water supply pump during the hydrogenation reaction will lead to rise in temperature, it being and exothermic reaction.
RECOMMENDATIONS
“Reactor high temperature alarm should be provided and it should be interlocked with control valve to be provided on the hydrogen gas bank PCV inlet for auto shutdown.
Pressure relief valve provided on the reactor should be periodically tested and calibrated.
Standby arrangement for cooling should be provided like overhead tank or a standby pipeline from another cooling tower should be provided.”

## Slide 14: NODE 4 – Hydrogenation Reactor
HAZARDS IDENTIFIED
Hydrogen gas venting not done before dropping the reaction mass. Hydrogen gas will escape from the reactor take off valve when it is opened for reaction mass drop.
RECOMMENDATIONS
“Hydrogen gas venting should be included as a check point in the batch check sheet.”

## Slide 15: NODE 4 – Hydrogenation Reactor
HAZARDS IDENTIFIED
Cooling coil leakage inside the reactor. Hydrogen gas being at higher pressure can enter the cooling water pipeline and enter the cooling water system.
Malfunction of the pressure reducing station can lead to high pressure in the internal coil of the reactor.
RECOMMENDATIONS
“Hydro test and thickness testing of internal coil of the reactor should be done periodically.
Pressure safety valve should be provided on the internal coil before inlet to the reactor. This should be periodically tested and calibrated.”

## Slide 16: NODE 4 – Hydrogenation Reactor
HAZARDS IDENTIFIED
Malfunction in the PCV station resulting in more pressure of hydrogen in the reactor. The pressure can exceed the reactor design pressure.
RECOMMENDATIONS
“The PCV, pressure gauges and safety relief valves should be periodically tested and calibrated.
The PCV system should be upgraded as mentioned in the drawing no. NI/H2/1240/P20047 R0.
Control valve should be provided at the PCV station inlet.
Two separate vents with flame arrestor should be provided for each set of PCV to prevent back pressure in the low pressure PCV set.”

## Slide 17: NODE 5 – Drop Tank
HAZARDS IDENTIFIED
Spillage of Hyflo & Tonsil Powder and exposure of personnel to these highly toxic products.
RECOMMENDATIONS
“Personal protection should be used as per the guidelines of the product MSDS.
Important instructions related to powder handling shall be displayed near the addition area.”

## Slide 18: NODE 5 – Drop Tank
HAZARDS IDENTIFIED
Temporary hose connection provided to internal heating coil of the drop tank.
RECOMMENDATIONS
“Permanent piping should be provided for steam supply to the internal heating coil of the drop tank.”

## Slide 19: NODE 5 – Drop Tank
HAZARDS IDENTIFIED
Overfilling of the drop tank due to operator error. The capacity of the drop tank is smaller than the reactor. Contents may enter the vacuum system and can damage the vacuum pump components.
RECOMMENDATIONS
“Level indicator/transmitter should be provided for the drop tank.”

## Slide 20: NODE 6 – AMA Filter & Polishing Filter
HAZARDS IDENTIFIED
Less circulation will lead to early choking of polishing filter. This can lead to rise in pressure of the polishing filter.
RECOMMENDATIONS
“SOP should be updated to mention the frequency of polishing filter cleaning.
Pressure gauge and pressure relief valve should be provided on the polishing filter based on the design/working pressure of the polishing filter.”

## Slide 21: NODE 7 – Mechanical Seal Lube Oil & Cooling
HAZARDS IDENTIFIED
Lube oil unavailability or cooling failure will lead to damage of seal and subsequent failure. It will leakage of hydrogen gas during the hydrogenation process.
RECOMMENDATIONS
“Hydrogen gas leak detector should be provided near the reactor. It should be interlocked with auto shutdown of hydrogen supply.
Periodic inspection of the flameproof electrical equipment’s should be done.
S.O.P. should be prepared which contains provisions to prevent accumulation of static electricity and periodic inspection of the earthing & bonding should be carried out. Operators should be trained about the importance of flange bonding.”

## Slide 22: SITE VISIT
Hydrogenation Plant
  Openings on staircase and floors at higher levels.
  Hydrogen gas leak detector not in service.
  PSV provided on reactor and PCV station not tested and calibrated.
  Strings used for tying hoses in plant and hydrogen gas bank area.
  Temperature indicator for the reactor provided on the 1st floor and pressure indicator provided on the ground floor.
Other Observations
  Electrical cables inside the dyke wall at ground level at caustic lye storage.
  Leakages in pipelines, dyke wall broken/openings at caustic lye storage.
  Flange guards missing on caustic lye pipelines.
  Cooling tower near boiler – concrete structure cracks observed. Reinforcement steel exposed and corroded.